## Slide 1
FlashInfer moe_gemm_mxfp8_nt_groupwise()
Zero-padding grouped GEMM · MXFP8 UE8M0 group scaling · SM120 CuTe backend
01
NVIDIA | INTERNAL
out = moe_gemm_mxfp8_nt_groupwise(a, b, a_scale, b_scale, m_indptr, scale_granularity_mnk=(1, 1, 32))
输入 / 输出契约
A
[ΣMₑ, K]
FP8 E4M3 · token-packed
B
[E, N, K]
FP8 E4M3 · per expert
SFA
[Mₚ, Kₛ]
4×UE8M0 packed / int32
SFB
[E, N, Kₛ]
4×UE8M0 packed / int32
m_indptr
[E+1]
int32 CSR prefix sum
D
[ΣMₑ, N]
BF16 · token-packed
Grouped NT 语义
对每个 expert e：
p₀ = m_indptr[e]
p₁ = m_indptr[e+1]
Aₑ = A[p₀:p₁, :]
D[p₀:p₁, :] = Aₑ · B[e]ᵀ
N×T：A 不转置，B 在 GEMM 中按转置语义读取。
FlashInfer 执行映射
1
检查 dtype / shape / scale contract
2
按 shape 选择 TileM / TileK 配置
3
启动 grid = num_sms 的 persistent kernel
4
cooperative CTA 领取并计算 expert tile
5
按原 token-packed 行序写回 BF16 D
Zero-padding layout：A / D 保持 exact，只有 SFA backing storage 做每 expert 4-row 对齐
A / D
expert 0 · M₀
expert 1 · M₁
expert 2 · M₂
SFA
align4(M₀)
align4(M₁)
align4(M₂)
m_indptr = [0, M₀, M₀+M₁, ΣMₑ]
scheduler 用它恢复每个 expert 的真实 M 范围；A/D 不产生 padding rows。
Source: flashinfer/grouped_mm/cute_sm120_mxfp8_groupwise/core.py; csrc/cute_sm120_mxfp8_groupwise/
CuTe SM120 MXFP8

## Slide 2
Cooperative CTA Dataflow & SwapAB
统一 persistent mainloop；按 GemmType / shape 选择 epilogue，small-M 通过 SwapAB 映射到 internal TileN=8
02
NVIDIA | INTERNAL
① Setup
TMA descriptor prefetch
one elected thread
Initialize mbarriers
AB / SF full-empty pairs
Persistent tile scheduler
grid = num_sms · persistent CTA pool
② Warp-specialized mainloop
AB producer
TMA load A / B
AB stage ring
SF producer
TMA load SFA / SFB
SF stage ring
Math WGs
wait paired stages
S2R → MXFP8 QMMA
FP32 accumulator
full / empty mbarriers
TMA copy(next) overlaps QMMA(current) across K
③ Epilogue dispatch
TMA store
Normal / BMM / Masked Math WG: R2S · store warp: S2G
Predicated R2G
Grouped MoE · non-SwapAB Math WG: RMEM→SMEM→RMEM→GMEM
SwapAB + Predicated STG
Grouped MoE · small-M · logical M↔N internal TileN=8 = 8-row token slice · direct RMEM→GMEM
Unified kernel family：Normal · BMM · Masked · Grouped MoE | SwapAB small-M supported
Source: sm120_blockscaled/{builder,kernel_impl,launch}.cuh; sm120_common/epilogue.cuh
CuTe SM120 MXFP8

## Slide 3
Packed UE8M0 Scale → QMMA Fragment
GranK=32：4 个 scale 以 int32 搬运，在 register 中重解释成 QMMA 需要的 broadcast view
03
NVIDIA | INTERNAL
Global-memory scale contract
K 0–31
s0
K 32–63
s1
K 64–95
s2
K 96–127
s3
int32 packed word = [ s0 | s1 | s2 | s3 ]
PACK_NSF = 4 · PACK_NK = GranK × 4 = 128
Transport and view transform
GMEM
packed int32
TMA
copy packed word
S2R
packed register backing
transform_fragment_for_qmma
recast + layout transform
QMMA view
UE8M0 + stride-0 broadcast
SFA partition
按 output M 分发；同一 row scale 对 K32 atom 内所有 A 元素 broadcast。
SFB partition
按 output N 分发；同一 column scale 对 K32 atom 内所有 B 元素 broadcast。
transform_fragment_for_qmma() 只改变 type/layout view：无 unpack loop、无 FP32 scale multiply、无 dequant tensor。
Source: sm120_blockscaled/sf_mxfp8_tma_load.cuh:56–69, 129–270
CuTe SM120 MXFP8

## Slide 4
TileK64 / GranK32：Scale Fragment → QMMA View
SM120 16×8×32 block-scaled QMMA · S2R ownership 不变 · transform 是 zero-copy view
04
NVIDIA | INTERNAL
Tile-level logical SF：SFA [M128, 2] / SFB [N128, 2]。一个 packed int32 覆盖 K128；图中同时展开相邻两个 TileK64。
① tCrSFA / tCrSFB packed fragment
每个 element = 1×int32 = 4×UE8M0
TileK64 #0
TileK64 #1
byte 0
byte 1
byte 2
byte 3
tCrSF*[0]
UE8M0 #0
UE8M0 #1
UE8M0 #2
UE8M0 #3
tCrSF*[1]
UE8M0 #0
UE8M0 #1
UE8M0 #2
UE8M0 #3
tCrSF*[2]
UE8M0 #0
UE8M0 #1
UE8M0 #2
UE8M0 #3
tCrSF*[3]
UE8M0 #0
UE8M0 #1
UE8M0 #2
UE8M0 #3
* = A 或 B。每个粗框就是一个 packed int32；TileK64 #0 / #1 分别消费前 / 后两个 UE8M0。
VIEW ONLY
recast + layout
② QMMA logical tensor view
shape (32,4,(1,2),(1,2)) stride (0, 4,(0,1),(0,2))
k_in_sf = 0
k_in_sf = 1
K 0…31
K 32…63
K 64…95
K 96…127
MN0
UE8M0 #0 K32 broadcast
UE8M0 #1 K32 broadcast
UE8M0 #2 K32 broadcast
UE8M0 #3 K32 broadcast
MN1
UE8M0 #0 K32 broadcast
UE8M0 #1 K32 broadcast
UE8M0 #2 K32 broadcast
UE8M0 #3 K32 broadcast
MN2
UE8M0 #0 K32 broadcast
UE8M0 #1 K32 broadcast
UE8M0 #2 K32 broadcast
UE8M0 #3 K32 broadcast
MN3
UE8M0 #0 K32 broadcast
UE8M0 #1 K32 broadcast
UE8M0 #2 K32 broadcast
UE8M0 #3 K32 broadcast
zero-stride view：每个 QMMA atom 读取 1 个 UE8M0，并 broadcast 到对应 K32。
③ SFA lane mapping：32 lanes → 16 M rows
2 lanes share 1 M row
M axis
M0
K = 0…31：same UE8M0 scale byte (broadcast)
M1
K = 0…31：same UE8M0 scale byte (broadcast)
⋮
M15
K = 0…31：same UE8M0 scale byte (broadcast)
每个 M row 的 1 个 UE8M0 broadcast 到一个 K32 QMMA atom
④ SFB lane mapping：32 lanes → 8 N rows
4 lanes share 1 N row
N axis
N0
K = 0…31：same UE8M0 scale byte (broadcast)
N1
K = 0…31：same UE8M0 scale byte (broadcast)
⋮
N7
K = 0…31：same UE8M0 scale byte (broadcast)
每个 N row 的 1 个 UE8M0 broadcast 到一个 K32 QMMA atom
同一物理 register：S2R 决定 thread ownership；view 只改变 type / tensor coordinates；K32 identity 始终保持。
Source: sf_mxfp8_tma_load.cuh · mma_traits_sm120.hpp · sm120_blockscaled/kernel_impl.cuh
CuTe SM120 MXFP8

## Slide 5
5KP E2E Serving：CuTe vs DeepGEMM MXFP8 GranK32
Qwen3.5-35B-A3B-FP8 · TP1 · ISL=8000 / OSL=1000 · 3-round median · RTX PRO 5000 (5kp) GPU2
05
NVIDIA | INTERNAL
crossover 在 cc=16→32：cc=4–16 DeepGEMM 领先（CuTe 最大落后 10.4% @cc=4）；cc=32–128 CuTe 领先 +1.4% ~ +2.0%。
并发 cc | CuTe out tok/s (med) | DeepGEMM out tok/s (med) | 差异 % (CuTe vs DG) | 领先
4 | 332.5 | 371.1 | -10.4% | DeepGEMM
8 | 485.7 | 520.0 | -6.6% | DeepGEMM
16 | 674.0 | 692.3 | -2.6% | DeepGEMM
32 | 859.1 | 842.1 | +2.0% | CuTe
64 | 1043.7 | 1029.3 | +1.4% | CuTe
128 | 1082.6 | 1063.8 | +1.8% | CuTe
轮次协议：每 cc 依次 warmup→r1（首轮 sweep）与 warmup2→r2→r3（补充 sweep），r1/r2/r3 计入 median。output tok/s = 3 轮 median，差异% = CSV cute_vs_dg_tput_pct（=median(CuTe)/median(DG)−1，正=CuTe 快，持平不计入领先）。低并发负收益保留。cc=128 为 512 prompts / 客户端并发 128，TTFT 升高与排队同时出现（未做因果拆分）。两端 backend identity 实证：CuTe=CUTE_SM120_MXFP8_32 / DG=DEEP_GEMM_MXFP8_32。数据源：task_10 benchmark.csv——本脚本已独立复核 42/42（42 raw rows 唯一且全 OK，且 56 行逐行核对硬件/GPU/模型/配置/FI+DG commit 身份）。

## Slide 6
5KP Kernel Benchmark：CuTe vs DeepGEMM MXFP8 GranK32 MoE GEMM
RTX PRO 5000 Blackwell (5kp) · 单卡（1 GPU）· prefill 大 M · FC1 (G1) / FC2 (G2) · 3-round median
06
NVIDIA | INTERNAL
22 个可配对 case CuTe 全部领先 DeepGEMM，speedup 1.07× ~ 1.31×（同 MXFP8-K32 recipe / GranK=32 UE8M0）
模型 | m_pe | GEMM | CuTe TFLOPS | DeepGEMM TFLOPS | CuTe/DG
Qwen3.5-35B | 1024 | FC1 (G1) | 362 | 326 | 1.11×
Qwen3.5-35B | 1024 | FC2 (G2) | 294 | 275 | 1.07×
DeepSeek-V3 | 512 | FC1 (G1) | 380 | 328 | 1.16×
DeepSeek-V3 | 512 | FC2 (G2) | 358 | 304 | 1.18×
Qwen3-235B | 1024 | FC1 (G1) | 380 | 338 | 1.12×
Qwen3-235B | 1024 | FC2 (G2) | 356 | 322 | 1.11×
效率：CuTe peak MFU 86% · DeepGEMM large-M ~73–78%（同按 measured FP8 ceiling 442.8 TFLOPS 归一化）。DeepSeek-V3 m_pe=1024 因显存 OOM 未纳入配对。
数据源：task_09 benchmark_report.md / run_meta.txt · RTX PRO 5000 Blackwell · host R6KD-CX8aaS-GPU-16 · GPU3 (GPU-2fdb0b79) · FlashInfer db7abc0a · DeepGEMM a6b593d (=vLLM 2.5.0) · GranK=32 / UE8M0 · 3-round median · 仅 CuTe vs DeepGEMM kernel。